|  | CITY OF JOHNSTOWN Office of the City Clerk PO Box 160, 33-41 East Main Street Johnstown, New York 12095 (518) 736-4014 |
| --- | --- |

Article VI. Trees and Shrubs

Sec. 18-601. Jurisdiction, authority of city engineer.

The city engineer shall have exclusive jurisdiction, authority, control, supervision and direction over all trees, plants and shrubs, planted or growing in or upon the public highways and public places of the city and the planting, removal, care, maintenance and protection thereof.

Sec. 18-602. Regulations for planting, trimming and care of trees.

- Diameter of trunk. Trees must not be less than one inch in diameter of trunk one above the ground.

- Stakes. All trees from one to three inches in diameter of truck one foot above the ground must be protected and supported by three guards. When guarded with one stake only, the must be toward the prevailing wind.

- Location at, near intersections. No tree shall hereafter be planted at the intersection of two or more streets or within twenty feet of such intersection.

- Removal of stumps. In cutting down trees, the same must be removed with the root stump grubbed out when so required by the city engineer.

- Waterproofing cuts. All cuts above one inch in diameter must be water-proofed.

- Distance between trees. Trees shall hereafter be planted at least thirty feet except when a special permit is obtained from the city engineer.

- Clear space from curb to sidewalk. No tree shall be planted where the clear space between the curb and the sidewalk is less than three feet.

- Soil standards. No tree shall be planted where the soil is too poor to insure the growth of such tree unless the owner excavates a suitable hole of not less than thirty-six cubic feet and replaces the material removed with suitable loam or soil from pasture land.

- Distance from curb, sidewalk. No tree shall be planted nearer than one foot from the curb line or outer line of the sidewalk unless a special permit is granted by the city engineer.

- Type regulated. No tree shall be planted on any street except the variety selected by the engineer for that street. Varieties not allowed in the city include: poplar, box alder, bass wood, willow, evergreen, and linden.